## Slide 1: Arcade Simulation with FPGA Boards
Nick Burek and Thomas griebel
Loras College

## Slide 2: The Big Picture
Participating in Digilent Design Contest
Using an FPGA board
  The board allows for programmable hardware
  Embedded Microprocessor (MicroBlaze)
The board transmits a signal to a VGA monitor in 640x480 resolution
Create an easily programmable arcade system
  Capable of running different games by swapping out the source code

## Slide 3: 1982 classic Frogger

## Slide 4: Project Overview
Management/Software Engineering
Hardware
Hardware/software connection
Software

## Slide 5: Management/Software Engineering
Source Control
  Used GIT
  Divided labor between files
Created tasks and goals
  Bi-weekly meetings
  Discussed problems and solutions for design
  Decided on scope and limitations
  Communicated heavily over Skype

## Slide 6: Hardware
  VHSIC Hardware Description Language (VHDL)
  Components
    VGA Driver
    Joystick Driver
    Video RAM Interface

## Slide 7: VGA Driver
25 MHz clock
Horizontal and Vertical Sync signals
8 bit color

## Slide 8: VGA Driver cont.

## Slide 9: Joystick Driver
Serial Peripheral Interface (SPI)
5 bytes
  2 for X
  2 for Y
  1 for buttons

## Slide 10: Video RAM
On board Block RAM (BRAM) vs. Micron RAM chip
307,200 Bytes – if storing every pixel
Timing Concerns
  70 nanosecond read/write time from RAM
  40 nanosecond (25 MHz) time between pixel outputs
  Would require a cache and a FIFO buffer for writes
7,876 Bytes – if using a tile based system

## Slide 11: Hardware/software connection
  Tile-based system cache
    Inspired by the NES PPU
    Screen is divided 80x60 grid
    Storage for 64 8x8 tiles
    Repetition of tiles dramatically reduces file size
  Memory mapped operations
    32-bit objects are mapped to hardware
    Objects are divided into code segments
    The code segments instruct the graphics processor
  Microblaze
    Creates an actual computer environment to work with

## Slide 12: PPU and Tile-based theory

## Slide 13: Software
  Limited storage (16KB)
  Used C to create the logic for the game
  C++ used for development tools
    Compression
    Graphics conversion
  Problems
    Collisions
    Compression
    Animations
    Graphics

## Slide 14: Converting Graphics

## Slide 16: Storage and Space
Memory so limited even instructions set us over
Created innovative ways to pack memory
  Graphics are stored in 2D arrays which store color indexes

## Slide 17: Tile Rotating and Flipping

## Slide 18: Conclusion
What we gained from this
Work left to be done
Digilent Design Conference May 6th